## Slide 1: Roads that keep panels clean. Walkways that make power.
GridMats Solar × Reliance New Energy: cost-benefit case and pilot proposal
Prepared for Reliance Industries Ltd · October 2026
GridMats Engineered Surface Systems · www.gridmats.com
Notes: Open with the one-line idea: the same GridMats grid that Reliance already used at its Kutch solar block can (1) cut the life-cycle cost of solar-park roads, (2) keep dust off modules, and (3) as a GridMats Solar Walkway, turn walkways into generators. Every number in this deck comes from the companion Excel model; assumptions are labelled and the pilot is designed to measure them.

## Slide 2: The case in one page
GridMats on Reliance's solar parks pays back in under five years; a pilot this dry season proves it on Reliance's own data.
Solar-park roads
S1 on main roads, S2 on O&M tracks: NPV ₹4.1 Cr per 100 MW block over 25 years, 21% IRR, 4.7 yrs payback; premium only 0.9% of plant capex.
Cleaner modules
Dust-confining tracks cut traffic dust on nearby rows: about 590 MWh more a year per 100 MW (assumption the pilot measures).
Walkways that generate
GridMats Solar Walkway, about 160 W/m²: payback about 5.6 years in Navi Mumbai and 8.1 at Jamnagar.
Circular and low-carbon
Per 100 MW: 327 t of recycled PP put to use and about 10,900 t CO2e avoided over 25 years.
The ask
Pilot this dry season
1 km of solar-park road (S1 + S2) beside control sections, a 50 m² GridMats Solar Walkway, and 12 months of joint measurement.
Reliance pays ₹55.3 L
for ₹68.5 L of scope (ex-GST). Grid at ₹900/m², 23% below the 2025 trial price.
Decision at 12 months
If the measures are met, ₹900/m² is held for a park-wide 12-month rate contract.
Base case of the companion model (GridMats_Reliance_Solar_CostBenefit_Model.xlsx). Money ex-GST, 2026 prices, 10% discount rate.
Notes: Four messages, one ask. Lead with the roads: that is where the money is. The soiling benefit and the walkway economics are flagged as assumptions to be measured. The ask is small relative to Reliance's build programme: about one crore all-in including civil works by Reliance's own EPC.

## Slide 3: Kutch is being built now, on roads
Every block needs its roads before a single module goes up, and the choice of road shows up in O&M for 25 years.
5.5 lakh
acres at Kutch for Reliance's renewable giga-project
>40 bn
kWh a year planned output, about 3% of India's demand
55 MWp
of modules a day at peak installation
8-12 km
of internal road for every 100 MW of solar
What conventional roads cost a solar park
WBM / gravel: ruts, washes out and raises dust; regraded every monsoon
Concrete: 14-28 days of curing on the critical path
Bitumen: hot mix on site; renewal every 4-6 years
Dust on modules: West-India soiling 0.3-0.5% a day in the dry season
Reliance AGM 2026 as reported (BusinessToday, 19 Jun 2026); GridMats solar and wind parks flier; IRC:82-2015; soiling studies (Gandhinagar 0.37%/day).
Notes: Reliance's Kutch build-out is ramping from this post-monsoon season. Roads come first. Each conventional choice has a known cost: gravel needs regrading and throws dust on modules, concrete puts curing on the critical path, bitumen needs periodic renewal. GridMats is designed to avoid all three.

## Slide 4: Already proven on Reliance ground
Reliance New Energy, Z2 block, Kutch: GridMats OC-HD 40 access road on saline, low-CBR ground (ordered Sep 2025).
2,000 m²
OC-HD 40 grid on 200 gsm geotextile
IITPAVE
designed for CBR 3-5% saline subgrade
4 days
to train Reliance's own civil crew
Same day
opened to traffic the day it was filled
What the trial proved, and what it did not measure
It proved the build: Reliance's crew laid the grid and opened the road at once. It did not record rutting, dust or upkeep against a conventional section. The pilot adds exactly that, so the next decision rests on Reliance's own data.
2025 design, CBR 5% section (GM/OC/HD-5/GR)
12 mm-down aggregate in 40 mm OC-HD grid
70 mm
Upper sub-base, 20-40 mm blended gravel
300 mm
GSB Grade II
200 mm
200 gsm geofabric separator
Subgrade, CBR 5%
Reliance purchase and work orders (Sep 2025); GridMats design note 'Design of gravel roads for low CBR% soils', IITPAVE (Aug 2025). Not to scale.
Notes: Reliance has already bought and built GridMats once. Be candid: it was a trial without measurement. The pilot proposed here is designed to produce the performance data that the 2025 trial did not, against control sections built the conventional way.

## Slide 5: GridMats: surfaces made from waste plastic
Six systems, one GridMats platform: interlocking grids of 100% post-consumer recycled polypropylene.
100% recycled PP
6.6 kg of post-consumer plastic in every m² of OC-HD 40
407 t/m²
lab test on the empty OC-HD 40 panel (Bureau Veritas, 2021)
2.0× base modulus
at CBR 5% with the grid at the GSB/WMM interface (IIT Hyderabad, interim report)
Patent and GreenPro
Indian Patent 398992; CII GreenPro certified
32 sites, 65,081 m²
built across 12 states; over a million sq ft supplied
Trusted by industry
Reliance, Toyo Engineering, Tata Advanced Systems, GMR Hyderabad Airport, Godrej, Aditya Birla
Recent heavy-duty result: Godrej, Vikhroli (May 2026). 400 m² of OC-HD 40 built in 3 days, carrying about 50-80 trucks a day with no cracks since June, at 21% less than a conventional concrete road.
GridMats master data Rev 1.3; Bureau Veritas BVIPL:SPL:BL/2545/7/2021/A; IIT Hyderabad interim report (Oct 2025); Godrej site observation (approximate truck count).
Notes: Credentials, with the approved wording. 407 t/m² is a lab test on the empty panel, not a pavement capacity. IIT Hyderabad work is an interim report presented at TGS2026. The Godrej Vikhroli road is the most recent heavy-truck proof.

## Slide 6: GridMats Solar: four tools for Reliance
Each part of a solar park gets the surface it needs; all of them share one grid, one method statement and one supplier.
S1 Cement-treated gravel
Main roads, inverter and transformer yards
Vehicles up to 49 t gross (GVW)
Light traffic at 3 days, trucks at 7
No saw-cut joints, no hot mix
S2 Permeable stone chip
O&M tracks, laydown and substation yards
Opens the same day it is filled
Rain goes through; no surface drains
Chips held in cells, so less dust
S6 Top-covered mats
Crane pads and temporary access
Laid or lifted in a day
Moves with the installation crew
Reused block after block
Solar Walkway + IoT
Walkways, EV hubs, campus paths (pilot stage)
About 160 W of PV per m²
No extra land, roof or mounting
Sensors report load, moisture, heat
GridMats solar and wind parks flier (Oct 2026); GridMats Solar Walkway flier (6 Oct 2026). Solar Walkway and IoT are at pilot stage.
Notes: S1 for heavy roads and yards, S2 for O&M tracks (what Reliance used at Kutch), S6 mats for temporary crane and access pads, and the Solar Walkway with IoT sensing for campuses. One supplier, one method statement for every EPC contractor, hold-point QC by GridMats engineers.

## Slide 7: Pavement design for Kutch's saline ground
GridMats base tables for CBR 2-5%; final thickness from IITPAVE on the pilot block's measured CBR.
S1 main road and yards
Load class D: vehicles up to 49 t GVW
OC-HD 40 + cement-treated gravel
40 mm
M-sand bedding
25 mm
WMM
150 mm
GSB
200 mm
Geotextile 200 gsm
Subgrade, CBR 2-5%, 98% MDD
Installed about ₹2,029/m² · bitumen ₹2,000 · concrete ₹3,200
S2 O&M track
Load class C: trucks and water tankers
OC-HD 40 + 8-12 mm stone chips
40 mm
Bedding
20 mm
WMM
150 mm
GSB
100 mm
Geotextile 200 gsm
Subgrade, CBR 2-5%, 98% MDD
Installed about ₹1,682/m² · WBM ₹600
GridMats Systems Manual Rev 1.3 base tables; unit rates from Design Engine 73 BoQ with grid at ₹900/m². U-nails 1 per 2-3 m², edge restraint throughout. Not to scale.
Notes: Both sections sit on geotextile over Kutch's saline, low-CBR formation, as at Z2. Final layer thicknesses are confirmed with IITPAVE once CBR and axle loads are measured at the pilot block. Costs are the model's bottom-up build-ups, ex-GST, with Reliance's EPC doing the civil works.

## Slide 8: Solar Walkway: paving that also powers
Walkable PV on wiring lumber over the GridMats base. Pilot stage: the pilot measures yield, heat and grip.
Walkable PV layer: 40 W module on each grid
MLP lumber, 40 × 40 mm, carries the wiring; 50 mm gaps drain
GridMats structural base, 100% recycled PP, on open-graded GSB
~160 W/m²
rated power (4 grids × 40 W per m²)
0
extra land, roof or mounting
15-16%
surface efficiency
Pilot method
Site check: shade, footfall, drainage, grid connection
Engineering: module and lumber layout, cabling, inverter, safety
Field pilot: measured W/m², kWh a day, module heat, grip, uptime
Scale-up with lighting, sensors and batteries
Co-development option: build the walkable module around Reliance's own Jamnagar HJT cells.
GridMats Solar Walkway flier (6 Oct 2026). Status: pre-commercial; pilot validation under way; no commercial deployment claimed. Concept diagram, not to scale.
Notes: Be clear this is pilot-stage. The design basis is about 160 W per m² of walkway: one 40 W module on each of four grids per m². What the pilot measures: real W/m², kWh per m² per day, module temperature, slip resistance and uptime. A natural extension for Reliance: co-develop the walkable module using Reliance HJT cells from Jamnagar.

## Slide 9: Day one vs 25 years
GridMats costs more than gravel to build and about the same as bitumen, and less than both once upkeep is counted.
Chart: O&M tracks (₹ per m²)
| WBM / gravel | GridMats S2
Build cost | 600 | 1681.5
25-year life-cycle cost (PV) | 2139.5255 | 2002.0295
Chart: Main roads (₹ per m²)
| Bituminous | GridMats S1 | Concrete
Build cost | 2000 | 2029.2 | 3200
25-year life-cycle cost (PV) | 3329.3798 | 2329.0336 | 3497.7259
6%
lower 25-year cost than WBM on O&M tracks
30%
lower 25-year cost than bitumen on main roads
33%
lower 25-year cost than concrete
Model sheet 'Road LCC'. Upkeep: WBM regrading ₹40/m²/yr and regravelling every 4 yrs; bitumen BC renewal every 5 yrs; GridMats 0.5%/yr plus top-ups. 10% discount rate, 5% cost escalation.
Notes: The honest picture. On O&M tracks GridMats S2 costs about 2.8 times WBM to build, but WBM is regraded every monsoon and regravelled every few years; over 25 years S2 comes out cheaper. On main roads S1 costs about the same as bitumen to build and avoids renewals every five years. Against concrete, S1 is cheaper on day one and over the life.

## Slide 10: ₹4.1 Cr NPV for every 100 MW block
One block: 10 km of internal road, 30% main roads (S1 instead of bitumen) and 70% O&M tracks (S2 instead of WBM).
Chart: Present value over 25 years, ₹ Cr per 100 MW
| Up-front GridMats premium | Road upkeep avoided | More energy from cleaner modules | Carbon value
₹ Cr (present value) | -3.4593 | 5.693 | 1.4016 | 0.45959
₹4.1 Cr
net present value over 25 years
21%
IRR on the GridMats premium
4.7 yrs
simple payback
0.9%
premium as a share of plant capex (₹4 Cr/MW)
Benefits are 2.2× the premium. Road upkeep alone covers it.
Model sheet 'Solar Park 100MW', base case. Energy valued at ₹2.70/kWh (solar PPA level); carbon at ₹700/t CO2e.
Notes: The bridge from premium to value for a 100 MW block. About 3.5 crore more up front, under 1% of a 400 crore plant. Road upkeep avoided alone is worth about 5.7 crore in present value; cleaner modules add about 1.4 crore and carbon about 0.5 crore. Net: about 4.1 crore per 100 MW, paying back in under five years.

## Slide 11: Positive NPV in every stress test
Each bar moves one driver to a pessimistic and an optimistic value; everything else stays at base.
Chart: NPV per 100 MW block, ₹ Cr
| WBM upkeep ±50% | Share of soiling from track dust | Discount rate | Bituminous upkeep ±50% | GridMats upkeep ±50% | Carbon value (₹ / t CO2e) | GridMats grid price ±10% | Road length per 100 MW (km) | Value of extra energy (₹ / kWh)
Pessimistic | 1.6702 | 2.8893 | 2.8789 | 2.8985 | 3.3202 | 3.6353 | 3.6172 | 3.6376 | 3.9392
Optimistic | 6.5197 | 5.9033 | 5.7079 | 5.2913 | 4.8696 | 4.6201 | 4.5726 | 4.5522 | 4.5102
₹3.3 Cr
Conservative
₹4.1 Cr
Base
₹7.7 Cr
Optimistic
₹2.3 Cr
Roads only, no soiling benefit
Model sheet 'Sensitivity'. The lowest result, ₹1.7 Cr, assumes WBM upkeep at half the base estimate.
Notes: Robustness. The biggest swing is how much WBM really costs to keep up; even at half the base estimate, NPV stays positive at about 1.7 crore per block. With no soiling benefit at all, roads alone still return about 2.3 crore per block. Discount rate 8 to 12% moves NPV between about 2.9 and 5.7 crore.

## Slide 12: Cleaner tracks, cleaner modules
Traffic on unpaved tracks throws dust on the nearest rows; chips held in GridMats cells throw far less.
WBM / gravel track
10 m
40 m
100 m
GridMats S2 track
10 m
40 m
100 m
589 MWh
more energy in year 1 per 100 MW (base assumption)
₹15.9 L
a year at ₹2.70/kWh
8,820 kL
of dust-suppression water avoided per 100 MW
Base assumption
3% yearly soiling loss; 15% of it from track dust; GridMats cuts that dust by 70%.
How the pilot measures it
Dust gauges and soiling reference cells on rows 10-100 m from the GridMats track and from a WBM control track.
Assumption informed by soiling studies (Gandhinagar 0.37%/day) and Univ. of Johannesburg (2025): soiling highest next to a gravel road, falling with distance.
Notes: This is the benefit unique to solar parks, and the one we are most careful about: it is an assumption until measured. Base case: of a 3% yearly soiling loss, 15% comes from track dust, and GridMats cuts that dust by 70%, so about 0.3% more energy, roughly 590 MWh a year per 100 MW. The pilot design puts reference cells and dust gauges at matching distances from a GridMats track and a WBM control track.

## Slide 13: Walkways that pay back in 5-8 years
A generating walkway costs more per kWp than a roof, but it replaces a walkway you would build anyway.
5.6 yrs
payback in Navi Mumbai (grid power about ₹12/kWh)
8.1 yrs
payback at Jamnagar (grid power about ₹7.5/kWh)
19%
pre-tax IRR over 20 years, Navi Mumbai
₹2,208
electricity bill saved per m² in year 1, Navi Mumbai
Chart: Capex per kWp, solar part only
| C&I rooftop | Solar carport | GridMats Solar Walkway
₹ per kWp | 40000 | 50000 | 71875
Why a walkway: no roof, land or mounting; a 50 m² pilot is about 8 kWp and 9,200 kWh a year. Across Reliance campuses and Jio-bp EV hubs (35,000 m², illustrative), about 5.6 MWp and ₹5.8 Cr a year.
Model sheet 'Solar Walkway'. PV layer ₹9,500/m² (GridMats pilot quote); yield 1,150-1,300 kWh/kWp for flat walk-on modules (assumption); 20-year life; paver walkway ₹1,100/m² avoided.
Notes: Walkway economics depend on the price of the power it replaces. At commercial tariffs in Mumbai, payback is under six years; at Jamnagar's lower industrial tariff, about eight. The per-kWp cost is higher than rooftop, so position it where roofs are full or shaded and the walkway is needed anyway, and for visibility at headquarters, Jio World Centre, data-centre campuses and EV hubs.

## Slide 14: Circular, low-carbon, water-wise
Per 100 MW block over 25 years, base case.
327 t
of post-consumer polypropylene turned into road
10,873 t
CO2e avoided: plastic reuse, bitumen avoided, cleaner energy
14,041 MWh
of extra clean energy from cleaner modules
8,820 kL
of dust-suppression water avoided in the build years
11,340 m³
of rain returned to the ground every year on S2 tracks
1,553 t
of cement avoided if main roads would otherwise be concrete
Fits Reliance's circularity story: GridMats complements ReRoute. ReRoute puts plastic into bituminous roads; GridMats goes where a road must be permeable, cement-free or open the same day.
Model sheet 'Sustainability'. Factors: recycled PP 1.2 kg CO2e/kg; cement 0.65 t/t; bitumen 0.55 t/t; CEA grid factor 0.710 t/MWh; Kutch rainfall 400 mm.
Notes: Sustainability numbers that can go straight into BRSR-style reporting, with the method shown in the model. Most of the CO2e comes from the extra clean energy, so it depends on the soiling assumption. Position GridMats alongside Reliance's own ReRoute, not against it.

## Slide 15: At Kutch scale, it adds up
Base-case results scaled from one 100 MW block. Kutch's planned output implies roughly 18-20 GW of solar.
 | 100 MW | 1 GW | 5 GW | 20 GW
Internal road (km) | 10 | 100 | 500 | 2,000
GridMats area (lakh m²) | 0.5 | 5.0 | 24.8 | 99.0
Up-front premium (₹ Cr) | 3.5 | 34.6 | 173.0 | 691.9
NPV to Reliance, 25 years (₹ Cr) | 4.1 | 40.9 | 204.7 | 819.0
Road upkeep avoided, undiscounted (₹ Cr) | 19 | 193 | 967 | 3,869
Recycled PP put to use (t) | 327 | 3,267 | 16,335 | 65,340
CO2e avoided, 25 years (t) | 10,900 | 1,08,700 | 5,43,700 | 21,74,600
₹41 Cr
NPV for every GW built with GridMats roads
3,267 t
of recycled PP per GW: a real outlet for post-consumer polypropylene
Model sheet 'Scale-up'. Indicative: linear scaling of one block; supply would run on a 12-month park rate contract.
Notes: Scale view. Per GW, about 100 km of internal road, about 41 crore of NPV and over 3,000 tonnes of recycled PP. The 20 GW column is indicative only; supply at that scale would run under a park-wide rate contract with phased deliveries.

## Slide 16: The pilot: 1 km of road + 50 m² of solar
Built this dry season in a Kutch block, measured through the 2027 monsoon, decided on Reliance's own data.
A Solar-park road, 1 km
0.4 km × 6 m main road in S1 and 0.6 km × 4.5 m O&M track in S2 (5,100 m²), beside WBM and bituminous control sections built by Reliance's EPC.
B Solar Walkway, 50 m²
About 8 kWp at Reliance Corporate Park, Navi Mumbai (or the Jamnagar Giga Complex), metered.
C Measurement, 12 months
IoT sensors and live dashboard, dust gauges, soiling reference cells, joint reports at 6 and 12 months.
2026
2027
Oct
Nov
Dec
Jan
Feb
Mar
Apr
May
Jun
Jul
Aug
Sep
Oct
Nov
Dec
Site walk, CBR and axle loads, IITPAVE design
QAP, test reports, factory visit; PO
Supply; dispatch date fixed in the PO
Build road (about 15 crew-days) + sensors
Solar Walkway built and metered
Monitoring through the 2027 monsoon
6-month joint report
12-month report and rate-contract decision
Indicative dates; supply date is confirmed in the PO once the site is ready. Control sections are built by Reliance's EPC as it would anyway.
Notes: Three parts. A: one kilometre of road in a block being built this season, half main road and half O&M track, beside conventional control sections. B: a 50 m² Solar Walkway where leadership walks past it every day. C: a year of joint measurement, through one monsoon, with a rate-contract decision at the end.

## Slide 17: An offer built to say yes to
List value of the pilot scope against what Reliance pays, ex-GST. Civil works are by Reliance's EPC at its own rates.
Scope | List | Reliance pays
OC-HD 40 grid, S1 main road | ₹22.44 L | ₹21.60 L
OC-HD 40 grid, S2 O&M track | ₹25.25 L | ₹24.30 L
Geotextile, U-nails, freight | ₹6.03 L | ₹6.03 L
Site design, BoQ, method statement, QC | ₹1.50 L | Included
Supervisor for the whole build | ₹2.25 L | Included
Supervisor travel and stay | ₹0.75 L | Included
Walkway base, OC-LW 40 | ₹0.54 L | ₹0.54 L
Walkway PV layer + inverter | ₹5.75 L | ₹2.88 L
IoT, soiling study, joint reports | ₹4.00 L | Included
Total | ₹68.50 L | ₹55.34 L
₹900/m² grid: 23% below the 2025 trial
the annual-contract rate, at pilot size
₹13.2 L of scope included (19%)
design, full-build supervision and travel, monitoring, half the walkway PV
₹900/m² held for 12 months
on a park rate contract; 3% year-end rebate above 50,000 m²
₹4.6 L credited back
10% of pilot grid value off the first order of 25,000 m² or more
Pilot road saves ₹27.7 L (PV)
over 25 years against building the same 1 km conventionally
Civil works by Reliance's EPC, indicative ₹42.3 L; total pilot budget about ₹97.7 L. 12-month defect liability with joint inspections at 6 and 12 months. GST extra.
Notes: The offer. Reliance pays about 55 lakh for 68.5 lakh of scope. The grid is at the annual-contract rate, 23% below what Reliance paid in 2025. Design, full-build supervision with travel, a year of monitoring and half the walkway PV are on GridMats. If the pilot meets its measures, the rate is held for a 12-month park contract and 10% of the pilot grid value comes back as a credit.

## Slide 18: How we will judge success
Agreed up front, measured jointly, reported at 6 and 12 months against the control sections.
Measure | Success looks like
Rut depth | ≤ 10 mm at 12 months
Exposed cell tops | ≤ 5% of area
Drainage | No standing water 1 hour after rain
Cracking | None crossing more than 3 cells
Dust and soiling | Lower dust deposition and soiling on rows near GridMats than near WBM
Upkeep | Fewer maintenance events and lower cost than control sections
Solar Walkway | Measured W/m², kWh/m²/day, module heat, grip, uptime
Live pilot dashboard
Temperature, humidity and subgrade moisture
Vibration from passing trucks
Rainfall and flood alerts
Site map with every sensor
Readings Reliance can export at any time
GridMats Pavement Monitor, already running on GridMats sites.
Thresholds from the GridMats Systems Manual maintenance limits. Dashboard: GridMats Pavement Monitor (temperature, humidity, moisture, CO2, vibration, rainfall, light, flood).
Notes: Success is defined before we start, using GridMats' own maintenance thresholds, and judged against Reliance's control sections. The live dashboard shows the sensor feed from the road; Reliance can export the data at any time.

## Slide 19: Lessons from 2025, built in
What we changed so the pilot runs to plan.
Supply on time
QAP, test reports and a factory-inspection slot are cleared before the PO, and the dispatch date is fixed in the PO once the site is ready.
Right aggregate
8-12 mm chip gradation agreed and sample-tested before dispatch; low fines so chips lock in and stay dust-free.
Design on measured soil
Sections from IITPAVE on the pilot block's measured CBR; WMM added where CBR is below 5%.
Supervision end to end
A GridMats engineer on site for the whole build with hold-point QC at every layer, not just the first days.
Data, not anecdotes
Control sections, sensors and joint inspections at 6 and 12 months, so the result is Reliance's own evidence.
Assurance: 12-month defect liability from handover with joint inspections at 6 and 12 months; repairs are cell by cell, with no traffic diversion.
Notes: Name the 2025 learnings without dwelling on them: supply timing, aggregate quality, design for very weak soil, and supervision length. Each now has a specific fix in the pilot plan.

## Slide 20: Next steps
Five steps from this conversation to a measured result.
1
This month
Name the pilot block and walkway site, and a Reliance sponsor
2
Oct-Nov 2026
Site walk, CBR and axle-load data; IITPAVE design and BoQ
3
Nov 2026
QAP and tests cleared; pilot PO with the dispatch date fixed
4
Dec 2026-Jan 2027
Build 1 km of road and the 50 m² Solar Walkway; sensors live
5
Jun and Dec 2027
Joint reports; decide the park-wide rate contract
GridMats · GroundReality Enterprises Pvt Ltd, Bengaluru
sales@gridmats.com · +91 63626 46287 · www.gridmats.com
Notes: Close on a date: name the block and the sponsor this month so that the road is built in this dry season and measured through the 2027 monsoon.

## Slide 21: Key assumptions and sources
All inputs are editable in the companion model (sheet 'Inputs'). Money ex-GST, 2026 prices.
Assumption | Base value | Source / basis
Discount rate; cost escalation | 10%; 5% a year | Assumption; 8-12% tested
Road per 100 MW; main share | 10 km; 30% | GridMats parks flier (8-12 km)
WBM; bitumen; concrete build | ₹600; ₹2,000; ₹3,200 /m² | TN G.O.; CPWD DSR 2023; GridMats pitch
GridMats S1; S2 installed | ₹2,029; ₹1,682 /m² | Bottom-up, Design Engine 73 rates, grid ₹900
WBM upkeep | ₹40/m²/yr + ₹250 every 4 yrs | Assumption; TRL/World Bank
Bitumen upkeep | ₹20/m²/yr + ₹450 every 5 yrs | IRC:82-2015
Yield; energy value | 1,870 kWh/kWp; ₹2.70/kWh | Gujarat plant data; SECI/NTPC PPAs
Soiling; track-dust share; cut | 3%; 15%; 70% | Assumption; measured in the pilot
Carbon value; grid factor | ₹700/t; 0.710 t/MWh | India CCTS range; CEA v21.0
Walkway power; PV price; yield | 160 W/m²; ₹9,500/m²; 1,150-1,300 | GridMats flier and quote; assumption
Full source list on the model's 'Sources' sheet: GridMats master data and price ladder (Sep 2026), Systems Manual, Design Engine 73, Reliance PO/WO (2025), RIL AGM 2026 coverage, CEA, GERC/MERC, SECI, IRC.
Notes: Reference slide for questions on assumptions. Every value is an input in the model and can be changed live.